## Slide 1: Seismicity TG Report
TG Activities as of August 2017

## Slide 2: Updated Hazard Calculations for SW BC

## Slide 3: Item 5.2.1
Update catalogue to at least end 2015

## Slide 6: Opportunities for future catalogue improvements
Yenier (2017) noted that GSC ML magnitudes were likely overestimated due to the use of Californian magnitude relations (i.e., Richter )
May be a need to remediate catalogue magnitudes for future hazard assessments
After Yenier (2017)

## Slide 7: Item 5.2.2: Add catalogue declustering
Have applied the Gardner & Knopoff declustering algorithm as implemented in the OQ Hazard Modeller’s Toolkit
Intended to remove “dependent events”
Calculated magnitude-frequency statistics for all zones based on non-declustered and non-declustered catalogues
Zone-specific results are here:
  Non-declusterd: https://github.com/treviallen/2020_gsc_nshm/blob/master/sources/area_sources/2020_H_model/full_catalogue/2020_H_model_MFD.full.MERGE.pdf
  Declusterd: https://github.com/treviallen/2020_gsc_nshm/blob/master/sources/area_sources/2020_H_model/declustered/2020_H_model_MFD.decl.MERGE.pdf
Note: some b-values and b-value uncertainties should be “fixed”
Consider grouping zones by geologic domains to ensure more robust statistics

## Slide 8: Declustering: Southwestern BC

## Slide 9: Non-declusterd Catalogue

## Slide 10: Declusterd Catalogue

## Slide 11: Declustering: Western Arctic

## Slide 12: Non-declusterd Catalogue

## Slide 13: Declusterd Catalogue

## Slide 14: Non-declusterd Catalogue

## Slide 15: Declusterd Catalogue

## Slide 16: Declustering: Rocky Mtns

## Slide 17: Non-declusterd Catalogue

## Slide 18: Declusterd Catalogue

## Slide 19: Non-declusterd Catalogue

## Slide 20: Declusterd Catalogue

## Slide 21: Non-declusterd Catalogue

## Slide 22: Declusterd Catalogue

## Slide 23: Declustering: Eastern Canada

## Slide 24: Non-declusterd Catalogue
This is a bug in my plotting, not my consideration of completeness!

## Slide 25: Declusterd Catalogue

## Slide 26: Non-declustered b-value

## Slide 27: Declustered b-value

## Slide 28: Rates of MW 5.0 (Non-declusterd)

## Slide 29: Rates of MW 5.0 (Declusterd)

## Slide 30: Rates of MW 6.0 (Non-declusterd)

## Slide 31: Rates of MW 6.0 (Declusterd)

## Slide 32: 5.3.1: Seismic Source Model
Alternative source model in the West:
  smoothed seismicity, BC Hydro, other?
Inclusion of Leech River / Devil’s Mountain Fault Systems (southern Vancouver Island)
Stepped Cascadia in-slab sources
Revision of slip rates for some fault sources (e.g. Eastern Denali, YK)
Simplification of Eastern source model?

## Slide 33: Modified Western Source Model
Modification of some area sources to better reflect historical seismicity and geologic structure:
  Added sources bounding the Rocky Mountain Trench
  Split Coast Mountains (CST) into two narrower zones to better reflect geologic structure and seismicity
  Split Puget Sound Deep and extended landward

## Slide 34: Modified Western Source Model
2015 NBCC
Modified

## Slide 35: 5.3.2: Smoothed Seismicity
Initial smoothed seismicity models developed using fixed-kernel smoothing have been generated:
  Using OQ HMTK implementation
  Uses a smoothing kernel of 50 km, b-value=1.0 and Mmin=3.0
  Use declustered catalogue
  A grid of activity rates has been produced
Not yet convinced by the results
  Elliptical nature of smoothed model suggests distances are based on lat/lon in degrees rather than in km

## Slide 39: 5.3.3 Leech River / Devil’s Mtn Fault System
Two studies have identified potentially active crustal faults in the southern Vancouver Island region
Tectonically driven Holocene faulting identified in the Leech River Valley
DMF included in USGS model
LRF used in BC-Hydro model

## Slide 40: LRF/DMF Logic Tree
slip rate is given based on slip rates of Johnson et al. (2001)
Seismogenic thickness = 15 km (down-dip fault width approx. 16 km)
Fault dip = 70 degrees to North

## Slide 41: Short Period Impacts of SWBC Faults

## Slide 42: Long Period Impacts of SWBC Faults

## Slide 43: 5.3.8: Dipping Source for Puget Sound: Option 1
Distribute activity rates for the intraslab GTP zone across three appox equal area sources at different depths
The 2015 model used a simple “flat” source zone at 50 km that undelays the crustal source zone
Seismicity TG suggests representing the dipping slab more appropriately
2015 GTP source becomes deeper as it approaches mainland
Hazard is reduced by about 4-12%

## Slide 44: 5.3.8: Dipping Source for Puget Sound: Option 2
Split GTP and treat as two (or three) independent sources
Move deep sources further landward to capture deep earthquakes
  This may increase Vancouver’s short-period hazard from 2015

## Slide 45: GTP - West

## Slide 46: GTP - East

## Slide 47: 5.3.4 Updated Cascadia Interface Rates
New data suggests the average return period for Cascadia megathrust earthquakes is shorter (Goldfinger et al. 2016)
  2015 NBC assumed return period of 550 yrs
  Identified 23 Holocene turbidites
  New return period is estimated at 430 yrs
Chart: Distance (km)
| 1.0 | 8.0 | 53.7 | 76.0 | 107.3 | 140.0 | 160.6 | 213.8 | 267.6 | 321.2 | 374.5 | 399.0 | 427.7 | 480.7 | 534.1 | 587.4 | 640.5 | 693.4 | 746.1 | 798.6
2020 Sa0.2 | 1.5732 | 1.5206 | 0.965 | 0.787 | 0.479 | 0.3286 | 0.2693 | 0.1653 | 0.1059 | 0.07 | 0.0456 | 0.0389 | 0.0312 | 0.0218 | 0.0153 | 0.0108 | 0.0069 | 0.0048 | 0.0037 | 0.0024
2015 Sa0.2 | 1.4642 | 1.4186 | 0.891 | 0.7289 | 0.4465 | 0.3066 | 0.2494 | 0.1518 | 0.0968 | 0.0639 | 0.0418 | 0.0354 | 0.0284 | 0.0199 | 0.0141 | 0.0097 | 0.0062 | 0.0044 | 0.0034 | 0.0021
2020 Sa2.0 | 0.5858 | 0.5712 | 0.4268 | 0.3695 | 0.2715 | 0.2131 | 0.1882 | 0.1392 | 0.1057 | 0.0816 | 0.0627 | 0.0565 | 0.0486 | 0.0389 | 0.0312 | 0.025 | 0.0202 | 0.0163 | 0.0134 | 0.0091
2015 Sa2.0 | 0.5382 | 0.5257 | 0.3912 | 0.3415 | 0.2511 | 0.1961 | 0.1734 | 0.1267 | 0.0963 | 0.0745 | 0.0567 | 0.0511 | 0.0445 | 0.0353 | 0.0283 | 0.0227 | 0.0185 | 0.0149 | 0.0121 | 0.0077

## Slide 48: 5.4: Ground-Motion Models for 2020 NBC
2015 NBC used Atkinson & Adams (2013) GMMs using the referenced backbone approach:
  Upper & lower models capture variability among models
  Simplifies hazard calculations/computationally efficient
Several advances have been made in GM modelling since the AA13 models developed:
  NGA-West2 (AA13 informed by these models)
  NGA-East (seed models published – models for USGS hazard maps are available)
    Being implemented into OQ
  NGA-Subduction (underway - no models available)

## Slide 49: 5.4.1: Ground Motion Model – Crustal EQs
NGA West 2 (2014): 2/3 Weight (California/Global)
  Abrahamson et al (1/6)
  Boore et al (1/6)
  Campbell & Bozorgnia (1/6)
  Chiou & Youngs (1/6)
Akkar et al (2014): 1/3 Weight (Europe/Middle East)
  Shown to perform well for 2012 Haida Gwaii sequence (Allen & Brillon, 2015)
  NGA-West1 found to be suitable for Europe (Stafford, 2009)

## Slide 50
Short Period

## Slide 51
Short Period

## Slide 52
Long Period

## Slide 53
Long Period

## Slide 54: NGA-W2 Short Period Differences

## Slide 55: NGA-W2 Long Period Differences

## Slide 56: Impact of Change in Crustal EQ GMPEs
Not much!
Slight increases at short periods
No significant changes at long periods

## Slide 57: 5.4.3: Ground Motion Model – Intraslab GMMs
Proposed GMMs:
  Atkinson & Boore (2003): 1/8
  Atkinson & Boore (Cascadia; 2003): 1/8
  Garcia et al. (2005): 1/4
  Zhao et al. (2006): 1/8
  Zhao et al. (Cascadia; 2006): 1/8
  Abrahamson et al (BC-Hydro; 2015): 1/4
Brillon (in prep) demonstrated that AB03 and Gea05 models best matched recorded data from Cascadia

## Slide 58: Intraslab GMM Behavior

## Slide 59: 5.4.3: Ground Motion Model – Interface GMMs
Proposed GMMs:
  Zhao et al. (2006): 1/8
  Zhao et al. (Cascadia; 2006): 1/8
  Atkinson & Macias (2009): 1/4
  Ghofrani & Atkinson (2014): 1/8
  Ghofrani & Atkinson (Cascadia; 2014): 1/8
  Abrahamson et al (BC-Hydro; 2015): 1/4
Similar representation of GMMs from 2015 model
  Down-weight “Cascadia” models as they are less likely to be appropriate for Vancouver Island

## Slide 60: Interface GMM Behavior

## Slide 61
Short Period

## Slide 62
Short Period

## Slide 63
Long Period

## Slide 64
Long Period

## Slide 65: 5.4.3: Ground Motion Model – Eastern GMMs
Potential GMMs:
  Atkinson & Adams (2013) – as used for 2015 NBC
  Or
  Use NGA-East seed models (e.g. Yenier & Atkinson, 2015)

## Slide 66: SCR GMM Behavior
Data from the 2012-06-19
Mw 5.0 Moe, Australia earthquake

## Slide 67: Updated Hazard Calculations for SW BC

## Slide 68: 5.5: Engineering Applications
Near-fault design ground motions
  Define “near-fault”
  Guidance on selecting ground motion time-histories for near-fault sites
  Other considerations?
Consideration of long-duration Cascadia subduction motion (non-time-history analysis)

## Slide 69: 5.5.8: Cross-Committee Coordination with SC-HSB
TG recommended that SC-HSB be made aware of the trend in the updated seismicity values particularly in the west, and potential values exceeding current threshold
  Sa(0.2) ≤ 1.8

## Slide 70: Documentation
A series of White Papers are currently being drafted:
  Modified dipping slab sources
  SW BC faults
  Floating ruptures
  GMM cut-off distances
  Rationale for GMM selection